Channel transmission generalisation

Generate a signal stream, make packets out of it, transmit in a Jakes based wireless channel, add AWGN with a specified, perform LS noise removal and infer for different parameter variations(size of the packets analysed, ratio of header to data in packet)

1. transmit.py

This code does everything that is specified above except for the inference part. The steps taken are outlined below:

a. generate and store the values of the channel for sufficient instances using the jakes_totext.py file.
b. initialize a random signal with a specified mean and variance composing of exclusively 1 and -1(essentially a digital communication model). Alternately, take an audio signal(not advised to do so, because it is not representative of real life digital communications.
c. scale the random signal packetwise with the corresponding channel values for every data point(bit). Add awgn calculated using the specified SNR either calculated packetwise or for the entire signal. In the latter case, it means there is noise being transmit even when no packet is being sent and hurts the model’s performance.
d. we now assume that the pilot/header sequence(a part of the packet) is known. Using the corresponding recieved signal y, compute the value of the best fit channel using the least squares method(the channel is assumed to be constant over the width of the packet in this model).
e. divide y by the found value of the channel to retrieve the originally transmit signal plus some noise caused error. This will be insignificant when the SNR is large.
f. plot and do whatever to make inferences.

2. mse_v_....py

These two files are used to observe and understand what is common sense to us. The assumption of a constant value of the channel over the packet fails and increases the mse as the packet size increases. Also the mse is low when the header to payload ratio is larger for a packet(not completely increasing though, I wonder why). Some base plots are attached with this document.